## Slide 1: EBU Workshop, 09/24/2014 Geneva Developing for SSM and AMT
Duanpei Wu, duanpei@cisco.com
Toerless Eckert, eckert@cisco.com
Sept. 19, 2014

## Slide 2: Content
AMT Relay Setup and Check – with ASR 1k
  Check Router Configuration
  Use 4 programs developed based on AMT GW library
AMT Gateway Library
  What is implemented and what is not yet implemented
  Lib Architecture
  Detail APIs
Test and Sample Code
  4 examples

## Slide 3: Project background and where to get source code?
There are several AMT related projects in Cisco. Open source amt_gw_lib is an effort under one of these projects.
The current version is 20140920, the initial public-accessible version
The source code could be retrieved from
  https://github.com/cisco/SSMAMTtools or
  https://cisco.app.box.com/files/0/f/2384374279/1/f_20937570747

## Slide 4
AMT Relay Setup and Check
– with ASR 1k

## Slide 5: AMT Environment in this Workshop
SSM flows (232/8)
SSM flows (232/8)
AMT Relay (ASR 1k)
relay : G0/2/0: 192.168.0.1
anycast: G0/2/1: 192.168.1.1
SSM enabled I/F: G0/2/2: 192.168.2.1
Multicast disabled
N3048TP
(IP up:192.168.1.100
IP down: 192.168.3.1
WIFI: 192.168.3.2 192.168.101.1)
Multicast enabled
N3048TP
(IP up:192.168.2.100
Ip down: 192.168.4.1
(WIFI: 192.168.4.2, 192.168.100.1)
SSM source streamer
(IP:192.168.0.100)
AMT GW lib test bed
(eth0: 192.168.100.100
eth1: 192.168.101.100)
SSM flows (232/8)
Client /w AMT GW lib application
AMT flow
SSM flows (232/8)
AMT flow
PC terminals
IP:192.168.101.x
Client /w AMT GW lib application
Test-bed access
SSM flows
AMT flow
Network connection
(192.168.0.100, 232.10.10.10)
  –- random packets @ 1 pps
(192.168.0.100, 232.10.10.100)
  – random packet @1 pps
(192.168.0.100, 232.200.0.1)
  – an mp4 stream @~450 kbps
(192.168.0.100, 232.200.0.2)
  – an mp4 stream @~1.3 mbps

## Slide 6: Relay Configuration: Example
interface Tunnel1 !!! AMT tunnel for interface G0/2/0 (192.168.0/24)
ip address 55.55.55.55 255.255.255.255
no ip redirects
ip pim sparse-dense-mode
ip igmp version 3
tunnel source GigabitEthernet0/2/0
tunnel mode udp multipoint
amt relay traffic ip
!
interface GigabitEthernet0/2/0
ip address 192.168.0.1 255.255.255.0 !!! the relay IP address
ip pim sparse-dense-mode
negotiation auto
!
interface GigabitEthernet0/2/1
ip address 192.168.1.1 255.255.255.0 !!! the anycast IP address
negotiation auto
!
ip pim ssm default
ip amt gateway anycast-relay-address 192.168.1.1 !!! make it anycast address
Use static routing
Use dynamic one
interface Loopback2
ip address 154.7.0.71 255.255.255.255 !!! Any-cast address
router ospf 100
network 192.168.0.0 0 0.0.0.255 area 100
network 192.168.1.0 0.0.0.255 area 100
network 154.7.0.71 0.0.0.0 area 100

## Slide 7: AMT Relay Check: anycast IP reachable
Check if anycast address is reachable by using “ping”

## Slide 8: AMT Relay Check: relay IP
Check if the relay returns the relay IP
amtchk is a program developed based on the amt_gw_lib presented in this workshop. It sets up a AMT channel between the client and the relay using the provided anycast IP. The source code is in …/amt_gw_10/test/amtchk.c

## Slide 9: AMT Relay Check: tunnel
Check if the AMT works correctly by subscribing a channel
  Feed packets to SSM
amtfeeder is a program developed based on the amt_gw_lib presented in this workshop. It generates a sequence of packets or read packets from a file and send them out to a SSM. The source code is in …/amt_gw_10/test/amtfeeder.c

## Slide 10: AMT Relay Check: tunnel
Check if the AMT works correctly by subscribing a channel
  Subscribe a channel
amtpoll is a program developed based on the amt_gw_lib presented in this workshop. It subscribes a AMT channel and prints out the packet received. The source code is in …/amt_gw_10/test/amtpoll.c

## Slide 11
AMT Gateway Library

## Slide 12: AMT Gateway Protocols Implementation and Status
Automatic Multicast Tunneling -- version 17
  Implemented:
  (1) Six messages: Relay Discovery, Relay Advertisement, Request, Membership Query , Membership Update and multicast dataMIP v4 complete; IP v6 in progress
  (2) IP v4
  (3) Periodic Three-way handshake : Request Membership Queuy membership Update
  (4) Retry with timing: initial time  2^#iterations
  (5) default timeout: as specified in protocols such as 125seconds for query interval
  Not yet implemented today:
  (1) one message: Teardown (optional gateway message)
  (2) IP v6

## Slide 13: AMT Gateway Protocols Implementation and Status
  Internet Group Management Protocol, IGMPv3 Implemented: Version 3 for IP v4
Multicast Listener Discovery, MLDv2
  Not yet implemented: Version 2 for IP v6
Socket Interface Extensions for Multicast Source Filters
  Through socket lib,
  setsockopt (…, IP_ADD_SOURCE_MEMBERSHIP, …)
Others
-- GNU C lib: such as Socket
-- …

## Slide 14: AMT Gateway Library: All APIs
Feature APIs
  amt_openChannel() -- open a channel through ssm or amt with an option to try both and to use whichever gets first connected
  amt_closeChanne() -- close the opened channel
  amt_poll() -- poll the channel status: data-in, data-close, data-err
  amt_recvfrom() -- receive packets (buffered) from the network through AMT/SSM
Sink API
  amt_addRecvHook() -- callback functions to send received packets from AMT/SSM to the App
Status Check API
  amt_getState() -- Get the channel or relay state: joining, joined, etc.
Initialization/reset APIs
  Amt_init() -- do initialization (optional)
  amt_reset() -- reset the module to clear up resources and set the module to the initial state
Trace APIs
  amt_setTraceSink() -- set trace the hook
  amt_setTraceLevel() -- set trace level
Other APIs
  amt_getVer() -- get the version of the module: the date code posted

## Slide 15: Typical Call-flows
  amt_setTraceSink() /amt_setTraceLevel()
  Amt_init()
  Amt_openChannel()
  Amt_poll()
  Amt_recvfrom()
  Call-APP()
  Amt_closeChannel()
  Amt_reset()
  amt_setTraceSink() /amt_setTraceLevel()
  Amt_init()
  Amt_openChannel()
  Call-APP()
  Amt_closeChannel()
  Amt_reset()
Or
  amt_addRecvHook()
  Amt_openChannel()
  Amt_openChannel()
  Amt_closeChannel()
  Amt_closeChannel()
Packet sink
  Amt_openChannel()
  Amt_closeChannel()
  Amt_getState()
  Amt_getState()

## Slide 16: AMT Gateway Library: Architecture
AMT APIs:
  -- A layer to provide AMT features to the Apps
AMT feature Implementation:
  -- The actual AMT feature implementation module for such as tunnel setup, query, packet receiving and dispatching.
Timer Module:
  -- A simple timing wheel to provide the keep-alive three-way handshaking and request retrying timer
AMT Trace:
  -- A trace module for debugging. The trace could be shown internally using “print” or through a hook API to the App.
AMT Utility:
  -- A bound of handy code to provide cross-platform utility features, such as getting the current time and creating a thread. (Currently, only Linux supported)
ex_sock:
  -- Code to implement the required socket features for the AMT module lib. The code is intended to be replaced for different applications.
AMT APIs
AMT Feature Implementation
AMT Trace
AMT Utility
timer module
ex_sock
(External Socket code (lib) for AMT)

## Slide 17: Socket code
AMT Lib
amt_sock Wrapper
EX_SOCK
EX_SOCK
AMT GW Lib
The ex_socke code provides the necessary socket functions
amt_sock wraps the ex_sock code or lib. The other amt lib code calls the APIs provided in amt_sock.
The ex_sock could compiled as integrated part of lib or used as an external lib.
Other AMT code
int amt_setSSMTTL(s32 s, u32 ttl)
{
return(ex_setSSMTTL(s, ttl));
}
int amt_joinSSMGroup(s32 s, u32 groupIP, u32 sourceIP, u32 interfaceIP)
{
return(ex_joinSSMGroup(s, groupIP, sourceIP, interfaceIP));
}

## Slide 18: AMT Gateway Library: Source Code Structure
src:
amt.c amt_impl.c amt_impl.h amt_sock.c amt_sock.h amt_trace.c amt_trace.h amt_utility.c amt_utility.h
include: amt.h
Lib:
android:
ios:
linux: libamt.a
mac:
win32:
Build:
android:
ios:
linux: makefile
mac:
win32:
Test:
amtchk.c amtfeeder.c amtsink.c amtstream.c
android:
ios:
linux:
makefile
amtchk amtfeeder amtsink amtstream
trace-server: makefile traceServer.c traceServer
mac:
win32:
ex_sock:
ex_sock.c ex_sock_exp.h ex_sock.h
Docs:

## Slide 19: AMT Gateway Library: amt_openChannel()
/*
* open a ssm and amt channel or a try with both
* return a handle for success or NULL for failure
*/
amt_handle_t amt_openChannel( ipv4_t anycast, /* an IP to find a relays;
not used if req for ssm only */
ipv4_t group, /* group IP of SSM */
ipv4_t source, /* source IP of SSM */
unsigned short port, /* the destination IP of packets */
amt_connect_req_e req /* through ssm or amt or both */
);
Use this API to open a channel
The API is implemented asynchronously
The channel state could be accessed through amt_getState()
typedef enum {
AMT_CONNECT_REQ_NONE = 0,
AMT_CONNECT_REQ_SSM = 1, // req for ssm connection only. anycast not used.
AMT_CONNECT_REQ_RELAY = 2, // req for amt connection only
AMT_CONNECT_REQ_ANY = 3, // req for either ssm or amt connection. Whichever gets
// connected first is selected as the connection.
AMT_CONNECT_REQ_END,
} amt_connect_req_e;

## Slide 20: AMT Gateway Library: amt_closeChannel()
/*
* close an opened channel
* return 0 for success and -1 for failure
*/
int amt_closeChannel(amt_handle_t handle /* the handle open with amt_openChannel() */
);
Use this API to close the opened channel with amt_openChannel()
The API is implemented asynchronously for the connection through AMT and synchronously for SSM.
For the connection through AMT, the actual channel close is done through AMT message of Membership Update with (S,G) blocked.
Once the channel is closed, the handle is not valid anymore

## Slide 21: AMT Gateway Library: amt_poll()
/*
* poll to check if there are packets for the given handle array.
* return n events for success with event set in rs, and -1 for failure.
*/
int amt_poll(amt_read_event_t *rs, /* points to a handle array */
int size, /* handle array size */
int timeout /* in millisecond */
);
Use this API to to check the channel event for the opened channels with amt_openChannel()
The API is implemented synchronously.
If there is no event, this API will wait for timeout millisecond.
This API returns 0 for no event, n>0 for n events and -1 for failure.
typedef enum {
AMT_READ_NONE = 0,
AMT_READ_IN = 1, /* there is data in buffer */
AMT_READ_CLOSE = 2, /* amt channel close */
AMT_READ_ERR = 4, /* unexpected error */
AMT_READ_END
} amt_read_event_e;

## Slide 22: AMT Gateway Library: amt_recvfrom()
/*
* retrieve a packet from the channel the "handle" points to
* return the size of packet; -1 for failure
*/
int amt_recvfrom(amt_handle_t handle, /* the handle open with amt_openChannel() */
unsigned char *buf, /* buffer */
int maxBufSize /* max buffer size */
);
Use this API to receive the packet.
The API is none-blocked for packet available or not.
amt_poll() can be used to check the packet availability

## Slide 23: AMT Gateway Library: amt_addRecvHook()
/*
* add packet receiving sink
*/
typedef void (*amt_recvSink_f)(amt_handle_t handle, void *buf, int size, void *param);
int amt_addRecvHook(amt_recvSink_f recvSinkfuc, /* a sink function to receive packets */
void *param /* a parameter to pass from the sink function */
);
Use this API to add a packet receiving sink function.
The sink will be called once there is a packet available
Parameter param is passed through the sink function.
This API is exclusive with amt_poll() and amt_recvfrom()which are disabled once this API is called. amt_reset() will need to call to re-enable them.

## Slide 24: AMT Gateway Library: amt_setTraceSink()/amt_setTraceLevel()
/*
* set trace sink and level
*/
typedef void (*amt_traceSink_f)(int level, char *msg, int size);
int amt_setTraceSink(int level, /* 0-10 with 0 to turn off tracing and
10 to enable the max tracing */
amt_traceSink_f traceFunc /* a sink function to pass the traces */
);
int amt_setTraceLevel(int level /* 0-10 with 0 to turn off tracing and
10 to enable the max tracing */
);
Use these two APIs to add a trace sink function and set trace level.
If trace sink function is not set, the library will use the internal trace functions to print out trace.

## Slide 25
Test and Sample Code

## Slide 26: Test Environment
AMT Relay
(ASR 1k)
AMT Gateway
(Test Client, Linux)
Multicast Streamer/ packet feeder
Media source
Source Machine (Linux)
SSM
AMT
Four streams fed into SSMs, all with dstport=9010
(192.168.0.100, 232.10.10.10) – 1 pps
(192.168.0.100, 232.10.10.100) – 1 pps

## Slide 27: Example 1: find the relay address
#include <stdio.h>
#include "amt.h"
int main(int argc, char *argv[])
{
unsigned int anycast;
if (argc < 2) {
printf ("usage: %s anycast\n", argv[0]);
return 1;
}
anycast = ntohl(inet_addr(argv[1]));
// set trace level
//amt_setTraceLevel(AMT_LEVEL_10);
amt_init(anycast);
while((amt_getState(NULL) &
AMT_SSM_STATE_CONNECTED)!=AMT_SSM_STATE_CONNECTED) {
sleep(1);
}
amt_reset();
return 0;
}
Notes:
This program will establish a AMT connection.
By default, the trace will print out the relay address from anycast IP, for example, “ex1 192.168.1.1” will return 02:53:34.277 amt_impl.c:handleDiscoveryResp-- discovered relay address:192.168.0.1
To see all the traces, uncomment amt_setTraceLevel(AMT_LEVEL_10);
Code location: …/amt_gw_lib_10/examples/ex1.c > gcc -m32 -march=i686 -o ex1 ex1.c -I../include -L../lib/linux -lamt -lpthread

## Slide 28: Example 2: Subscribe to a AMT channel
...
// subscribe a AMT channel
{
unsigned char buf[1500];
unsigned int group = ntohl(inet_addr("232.10.10.10"));
unsigned int srcIP = ntohl(inet_addr(“192.168.0.100"));
amt_handle_t channelID = amt_openChannel(anycast, group, srcIP,
9010, AMT_CONNECT_REQ_RELAY);
amt_read_event_t rs={channelID,0};
while(1) {
int n = amt_poll(&rs, 1, 2000);
if (n>0) {
int len = amt_recvfrom(channelID, buf, 1500);
if (len > 0) {
printf("received packet with len = %u\n", len);
} else {
printf("Oh, get errors with amt_recvfrom() !!, Exit\n");
return 1;
}
} else if (n<0) {
printf("Oh, get errors with amt_poll()!!, Exit\n");
return 1;
}
}
}
...
Notes
this program will establish a AMT connection and read packets from the channel.
Error check is not complete
more detail code could be found in
…/amt_gw_lib_10/test/amtchk.c
Code location: …/amt_gw_lib_10/examples/ex2.c > gcc -m32 -march=i686 -o ex2 ex2.c -I../include -L../lib/linux -lamt –lpthread > ex2 192.168.1.1

## Slide 29: Example 2: Subscribe to a AMT channel – complete code
#include <stdio.h>
#include "amt.h"
int main(int argc, char *argv[])
{
unsigned int anycast;
unsigned char buf[1500];
unsigned int group = ntohl(inet_addr("232.10.10.10"));
unsigned int srcIP = ntohl(inet_addr(" 192.168.0.100"));
amt_handle_t channelID
amt_read_event_t rs;
if (argc < 2) {
printf ("usage: %s anycast\n", argv[0]);
return 1;
}
anycast = ntohl(inet_addr(argv[1]));
// set trace level
//amt_setTraceLevel(AMT_LEVEL_10);
amt_init(anycast);
while((amt_getState(NULL) &
AMT_SSM_STATE_CONNECTED)!=AMT_SSM_STATE_CONNECTED) {
sleep(1);
}
// subscribe a AMT channel
channelID = amt_openChannel(anycast, group, srcIP, 9010,
AMT_CONNECT_REQ_RELAY);
rs.handle = channelID;
while(1) {
int n = amt_poll(&rs, 1, 2000);
if (n>0) {
int len = amt_recvfrom(channelID, buf, 1500);
if (len > 0) {
printf("receive packet with len = %u\n", len);
} else {
printf("Oh,get errors with amt_recvfrom()!!\n");
return 1;
}
} else if (n<0) {
printf("Oh, get errors with amt_poll()!!, Exit\n");
return 1;
}
}
}
amt_reset();
return 0;
}

## Slide 30: Example 3: use amt_addRecvHook() to receive packets
static void packetRecv(amt_handle_t handle,
void *_buf,
int size,
void *param)
{
printf("receive packet with len = %u from channel:%p\n len, handle);
}
...
// add a callback function to receive all packets
amt_addRecvHook(packetRecv, NULL);
...
Code location: …/amt_gw_lib_10/examples/ex3.c > gcc -m32 -march=i686 -o ex3 ex3.c -I../include -L../lib/linux -lamt –lpthread > ex3 192.168.1.1
More detail code could be found in …/amt_gw_lib_10/test/amtsink.c
.

## Slide 31: Example 3: use amt_addRecvHook() – complete code
#include <stdio.h>
#include "amt.h"
static void packetRecv(amt_handle_t handle,
void *_buf,
int size,
void *param)
{
printf("ex3: receive packet with len = %u from channel:%p\n", size, handle);
}
int main(int argc, char *argv[])
{
unsigned char buf[1500];
unsigned int group = ntohl(inet_addr("232.10.10.10"));
unsigned int srcIP = ntohl(inet_addr(" 192.168.0.100"));
amt_handle_t channelID;
unsigned int anycast;
if (argc < 2) {
printf ("usage: %s anycast\n", argv[0]);
return 1;
}
anycast = ntohl(inet_addr(argv[1]));
// set trace level
//amt_setTraceLevel(AMT_LEVEL_10);
// call the initial function.
amt_init(anycast);
// add a callback function to receive all packets
amt_addRecvHook(packetRecv, NULL);
// open a channel
channelID = amt_openChannel(anycast, group, srcIP,
9010, AMT_CONNECT_REQ_RELAY);
pause();
amt_reset();
return 0;
}
Note that the error check is skipped.

## Slide 32: Example 4: Receive a Video Stream and Render it
AMT Relay
(ASR 1k)
AMT Gateway
(Test Client, Linux)
Audio/Video Renderer
(such as VLC)
Multicast Streamer or packet feeder
Media source
Source Machine (Linux)
SSM
AMT/SSM
unicast
(192.168.0.100, 232.200.0.1) – a mp4 stream @~450 kbps
(192.168.0.100, 232.200.0.2) – a mp4 stream @~1.3 mbps

## Slide 33: Example 4: Media Streamer and render
Source Streamer:
amtfeeder: a streamer which reads the RTP packets pre-recorded from a live streaming session (such as VLC streaming) and sends out the rtp packets in exactly timing to SSM.
Rendering with VLC as an example:
VLC: rtp://@:9010

## Slide 34: Example 4: stream receiving code for VLC
...
static void packetRecv(amt_handle_t handle, void *_buf, int size, void *param)
{
unsigned char *buf = (unsigned char *)_buf;
unsigned int *renderIP = (unsigned int *)param;
static ex_sock_t *pSock=NULL;
unsigned short sport=0;
if (pSock == NULL) { // to the render
sport=0;
pSock = ex_makeUDPSock(0, &sport, *renderIP, 9010);
EX_ERR_CHECK(pSock != NULL, " ", _EMPTY);
}
ex_sendPacket(pSock, buf, size);
}
...
Code location: …/amt_gw_lib_10/examples/ex3.c > gcc -m32 -march=i686 -o ex3 ex3.c -I../include -L../lib/linux -lamt –lpthread > ex3 66.163.54.1
Notes
An AMT channel is created to receive RTP packets
A socket is created to send the media stream to VLC player.
The code location: …/amt_gw_lib_10/examples/ex4.c
gcc -m32 -march=i686 -o ex4 ex4.c -I../include –I../ex_sock -L../lib/linux -lamt –lpthread
ex4 192.168.1.1 192.168.101.x
The full feature code could be found in
…/amt_gw_lib_10/test/amtstream.c

## Slide 35: Example4: complete code
#include <stdio.h>
#include <sys/time.h>
#include <netinet/in.h>
#include "amt.h"
#include "ex_sock.h"
#define _EMPTY
static void packetRecv(amt_handle_t handle, void *_buf, int size, void *param)
{
unsigned char *buf = (unsigned char *)_buf;
unsigned int *renderIP = (unsigned int *)param;
static ex_sock_t *pSock=NULL;
unsigned short sport=0;
if (pSock == NULL) { // to the render
sport=0;
pSock = ex_makeUDPSock(0, &sport, *renderIP, 9010);
EX_ERR_CHECK(pSock != NULL, " ", _EMPTY);
}
ex_sendPacket(pSock, buf, size);
}
int main(int argc, char *argv[])
{
unsigned char buf[1500];
unsigned int group = ntohl(inet_addr("232.200.0.1"));
unsigned int srcIP = ntohl(inet_addr(" 192.168.0.100"));
amt_handle_t channelID;
unsigned int anycast, renderIP;
if (argc < 3) {
printf ("usage: %s anycast renderIP\n", argv[0]);
return 1;
}
anycast = ntohl(inet_addr(argv[1]));
renderIP = ntohl(inet_addr(argv[2]));
// set trace level
//amt_setTraceLevel(AMT_LEVEL_10);
// call the initial function.
amt_init(anycast);
// add a callback function to receive all packets
amt_addRecvHook(packetRecv, &renderIP);
// open a channel
channelID = amt_openChannel(anycast, group, srcIP,
9010, AMT_CONNECT_REQ_RELAY);
pause();
amt_reset();
return 0;
}

## Slide 36: Further work on audio/video renderer
AMT Relay
(ASR 1k)
Audio/video Renderer
Multicast Streamer/ packet feeder
Media source
Source Machine (Linux)
SSM
AMT/SSM
AMT Gateway

## Slide 37: What we covered
Cisco drives effort to have open source AMT gateway library available to the public.
The initial version is available from the github.com under Cisco fork and the library will be updated time by time.
Introduction to the AMT lib and detail APIs
In addition to the AMT lib, there are 4 examples of code in the repository to demonstrate how to use the library.
5 test programs with the complete source code to check relay setup and AMT channels are included in the repository.